## Slide 1: Mw6.0 pre-event of 2024 Noto Penisula earthquake

## Slide 2: Near-field ground motions
Velocity filtered
between 0.03 and 30 Hz
Y-axis max +-1000 cm/s2
Y-axis max +-80 cm/s
Sado island
Noto Peninsula
1
2
3
Acceleration

## Slide 3
0.05-0.5
2024 1 1 16:10 8.3 37°31.0'N 137°14.4'E 10 - 能登半島沖
2024 1 1 16:10 9.5 37°30.4'N 137°13.8'E 10 5.9 石川県能登地方
2024 1 1 16:10 22.5 37°29.7'N 137°16.2'E 16 7.6 石川県能登地方
JMA catalog

## Slide 4
Position #3, depth =12 km
ISK001
ISK002
ISKH01
ISKH01
ISKH02
ISKH03
EW
NS
UD
#1 = JMA M7.6
#1b = JMA M5.9
Focal mechanism inversion (strike, dip, rake, t0, Mw)
Vel (cm/s)
Waveforms filtered between 0.05 – 0.5 Hz
Fitting only between 10-20 seconds
Focal mechanism by full waveforms
1D structure by Nishimura et al. (2023)

## Slide 5: Dynamic rupture inversion by patch
Nucleation patch (self-similar)
Target patch
~ 0.15 m
slip
shear stress
Slip direction
Model 0
1
8
Rupture directivity
MPa
0.05-0.5 Hz
10-20 sec

## Slide 6
Model 1: (69°, 65°, 104°)
Mw6.03 (not contolled, not optimized)
Rupture directivity
Strength drop = 10 MPa
Initial stress = 6 MPa
Dc = 0.15 m
Test 1

## Slide 7
Strike N79°E, Model 2x (= 6 Mpa)
Strike N79°E, Model 3x (= 12Mpa)
High stress drop
Test 2 (79°, 67°, 121°)
Fitting 0.05-0.5 Hz, 10-20 sec

## Slide 8
All SE dipping solution
All NW dipping solution
High stress drop
SZOT ISK001
Vertical Displacement
1 (Mw6.026)
2 (Mw6.034)
3 (Mw5.978)
1
2
3
Test 2 (79°, 67°, 121°) from JMA hypocenter
About 30 cm uplift before the mainshock (DPRI)
Uz (cm)

## Slide 9
Kato et al. (2023)
Where is the causal fault?
Test 2 (79°, 67°, 121°) from JMA hypocenter

## Slide 10
JMA
Where is the causal fault?
Model strike-dip-rake (°)
1_SW 46.9-26.0-124.4
1_NE 56.9-59.0-99.3
2 56-33-125
3 47-37-100
4 52-42-variabe
5 47-46-variable
Other models
1 69-65-104
2 79-67-121
3 56-33-125
Tested

## Slide 11: Influence of a smaller dip angle
JMA hypocenter at 10km
Model 3
Model 2
ISK001~SZOT
Model 2 is better
Uz (cm)
Prevous one

## Slide 12: Remarks
SE dipping fault is reasonable from the uplift at ISK001 (~SZOT).
Rupture directivity is up-dip direction, going away from the hypocenter of M7.6.
Preferred stress drop is 6 MPa or less so that the rupture extends below station ISK001.